Mitch Bradley
							September 19, 1985

		Proposed words for Standard Preface

	32-bit compatibility:

All the words described in "Compatible Forth on a 32-bit Machine"
Vol 2. No. 4 of the Journal ...
except for columns 2 and 3 on page 35 (these columns are words that
are only useful in special cases)

Justification:

These words make it possible to write Forth code that will run unchanged
on either a 16 bit machine or a 32 bit machine.

	Words from F83:

TRUE  FALSE  OFF  ON
BETWEEN  WITHIN
-ROT  NIP  TUCK
.ID
DEFER   IS   >DATA
BOUNDS
ASCII    CONTROL
NUMBER?
UP0 UP@ UP!  RP0 RP@ RP!   SP0 SP@ SP!
UPPER  LOWER

Justification:

These words are very useful.  I have trouble getting along without them.


	The rest of the comparison words:

0<> 0<= 0>= <= >= <> U<=  U>  U>=

Justification:

The set of comparison operators provided by the standard is somewhat
arbitrary.  Why should users have to remember which operators are
part of the standard and which aren't?


	Other useful words:

To cope with alignment requirements of various processors in a portable
fashion:

#ALIGN		-- n
	n is a machine-dependent number which describes the alignment
	requirements for the particular cpu.  An address where
	  addr #ALIGN MOD   is equal to 0 is suitable for storing any
	type of data.  For instance, #ALIGN is 2 for the 68000, 1 for
	the 8080, and 1 for the 68020.  For performance reasons,
	the implementation may chose a more restrictive alignment than
	is necessary.  For instance, the 68020 allows arbitrary alignment,
	(#ALIGN = 0) but it runs faster if #ALIGN = 4.

ALIGNED		addr1 -- addr2
	addr2 is the result of aligning addr1 to the next machine
	boundary modulo #ALIGN

ALIGN		--
	The dictionary pointer is aligned to the next machine boundary
	modulo #ALIGN.  The contents of dictionary locations skipped over
	in the process is unspecified.


To make many utilities independent of the threading technique employed:

TOKEN@		addr -- cfa
	addr is the address where a compilation address has been compiled
	into the dictionary.  cfa is the compilation address that is stored
	there.  This is not necessarily the same as @, because some systems
	may chose to store compilation addresses within a definition in
	an encoded form (e.g. as a relative address, as an index into a
	token table, etc).  When the cfa is on the stack it is in the
	form of an absolute address.

TOKEN!		cfa addr --
	The compilation address cfa is stored into memory at address addr
	in whatever form the system uses to store compiled addresses.
	See TOKEN@

TOKEN,		cfa --
	The compilation address cfa is compiled into the dictionary at
	here and the dictionary pointer is advanced.

/TOKEN		-- n
	n is the number of bytes of dictionary space occupied by a compiled
	compilation address.

TA1+		addr1 -- addr2
	Addr2 is /TOKEN more than addr1.  This is equivalent to the phrase
	  /TOKEN +

DEFINER		cfa1 -- cfa2
	cfa2 is the compilation address of the defining word which created
	the word whose compilation address is cfa1.





LBSPLIT		32b -- b.low b.mlow b.mhigh b.high
	The 32-bit number 32b is split into its constituent bytes, with
	the most significant byte appearing on the top of the stack.
	This should be implemented efficiently if possible; the high-level
	equivalent is rather slow.

BLJOIN		b.low b.mlow b.mhigh b.high -- 32b
	The inverse of LBSPLIT .

WBSPLIT		16b -- b.low b.high
	The 16-bit number 16b is split into its constituent bytes, with
	the most significant byte appearing on the top of the stack.
	This should be implemented efficiently if possible; the high-level
	equivalent is rather slow.

BWJOIN		b.low b.high -- 16b
	The inverse of WBSPLIT .




IMMEDIATE?	cfa -- flag
	flag is true if the word whose compilation address is cfa has
	immediate precedence.

PRINTABLE?	n -- flag
	flag is true if 8b represents a printable ascii character
	( bl <= n < DEL )

UALLOC		#bytes -- next-user-number
	#bytes is reserved in the user area at the next available location.
	next-user-number is the number of that available user location.

NUSER		--
	Used in the form
		NUSER <name>
	A user variable <name> is created and space is allocated for it
	in the user area.  The amount of space allocated is enough to
	store one stack item (16 bits on a 16-bit system, 32 bits on a
	32-bit system)

TH		--					Immediate
	Temporarily set the numeric base to HEX , interpret the next
	word in the input stream, and restore the base to its previous
	value.   This is especially useful for entering a hex number
	regardless of the current value of BASE .

TD		--					Immediate
	Temporarily set the numeric base to DECIMAL , interpret the next
	word in the input stream, and restore the base to its previous
	value.   This is especially useful for entering a decimal number
	regardless of the current value of BASE .

ALIAS		--
	Used in the form:
		ALIAS <name1> <name2>
	A new word <name1> is created whose behaviour is identical to
	<name2>.  The preferred implementation is state smart so that
	the compilation address for <name2> is compiled when <name1> is
	encountered while in compile state.  Note: this really isn't
	very hard to implement:

: alias  ( -- )     ( Input stream:  new-name old-word )
  create
    bl word find    ( cfa -1 | cfa 1  |  str false )
    dup if
       , , immediate
    else
      drop  ." can't find "  count type
    then
  does>  2@                ( cfa -1 | cfa 1 )
    state @
    if   0> if   execute   \ if immediate
            else token,    \ if not immediate
            then
    else
         drop execute
    then
;

Note that the portion of the does> clause after the 2@ is EXACTLY
the same behavior as the outer interpreter for a word that is found
in the dictionary.  In effect what ALIAS does is to look up the
cfa and precedence of <name2> when <name1> is created, then when
<name1> is later encountered, the does> clause performs the action
that would have been performed had <name2> been encountered instead.
This works right even if <name2> is immediate.

VFIND		str voc -- str 0  |  cfa 1  |  cfa -1
	Search only the vocabulary voc for the packed string str.
	The return value is the same as for FIND.  voc is same
	vocabulary address that is stored at CURRENT or CONTEXT
	(in other words it is not necessarily the cfa of the
	vocabulary), so that, for example,
	BL WORD CURRENT @ VFIND   would search only the compilation
	vocabulary.

>THREADS	cfa -- voc
	voc is the vocabulary address that is stored at CONTEXT when
	the vocabulary whose compilation address is cfa is executed.
	In other words,  ' ASSEMBLER >THREADS CONTEXT !   is equivalent
	to just   ASSEMBLER .   More usefully,
	   ' ASSEMBLER >THREADS VFIND   searches for a word in the assembler
	vocabulary without affecting the search order.


A final point:

I think it would be a good idea to have a set of 32-bit arithmetic
operators with names that start with L instead of D .  The reason is
that the 83 Standard has this wired-in notion that the stack has to
be 16 bits wide, which I think is a disaster given the realities of
hardware these days.  The double number wordset is sort of fuzzy on
the distinction between a 32-bit number and a pair of stack items.

A consistently-named set of words beginning with the letter L,
which always operate on 32-bit numbers regardless of the stack width,
is very valuable for writing portable code.
(You shouldn't always use explicitly 32-bit numbers, but when you
need 32 bits, it is hard to write portable code without a separate
set of operators that does the 32-bit thing regardless of the stack
width of the machine.)